## Slide 1: Quantifying knee osteoarthritis
Alice Chuang
April 28, 2011
En 250

## Slide 2: Introduction
Osteoarthritis increasing in aging population
Imaging techniques:
  Radiography (X-ray) – golden standard, qualitative
  MRI - quantitative, gaining popularity
  Spectroscopy
  Ultrasound
Difficult to quantify progress
  Joint space width – thickness of articular cartilage
  Osteophyte formation – bony protrusion
  Kellegren-Lawrence scale for severity of disease

## Slide 3: Approach
Fully automatic quantification of knee osteoarthritis severity on plain radiographs. Oka H, Muraki S, et al. Osteoarthritis Cartilage. 2008 Nov;16(11):1300-6.
KOACAD – Knee osteoarthritis computer-aided diagnosis
Thresholds normalized to Kellegren-Lawrence scale based on cohort of 2975 Japanese adults

## Slide 4: KOACAD
A) Boundaries C) Osteophyte area
B) Joint space width, area D) Femorotibial angle

## Slide 5
A) Original image
B) Filtered image
C) Region of interest
Vertical neighborhood difference filter
D) Upper rim = femoral condyle
Vertical filtering with 3x3 square neighborhood difference filter
KOACAD
Part 1

## Slide 6
E) Lower rim = Margins of tibial plateau
Anterior and posterior margins averaged
F) Straight regression line drawn of lower rim
G) Joint space area: inside rim, outside rim
Inner: Intersection of regression line, lower rim
H) Minimum joint space width
Minimum vertical space distance
KOACAD
Part 2

## Slide 7
I) Protrusion
Femur, tibia outlined by 3x3 square horizontal neighborhood difference filter
J) Osteophyte area = protrusion (inflection point)
K) Middle lines from outline of femur, tibia
L) Femorotibial angle: axes of femur, tibia
Straight-line regression of middle lines
KOACAD
Part 3

## Slide 8: Goal of Project
Create a Matlab program mimicking KOACAD
  Quantify disease state of osteoarthritis
  Use 2D radiographs
Successes
  mJSW – minimum joint space width
  JSA – joint space area
  FTA – femorotibial angle
Future
  Osteophyte area – protrusions near joint
  Automation
  Filter images

## Slide 9: First results: Test images
Simple cartoon images to test Matlab program
Top image, results in pixels
  Left
    JSA (joint space area) = 24
    min JSW (joint space width) = 1
  Right
    JSA = 27
    min JSW = 1
Bottom, result in degrees
  FTA (femorotibial angle)
  = 178.2
Notes: koacad(test,5,1,1,800,5)

## Slide 10: Test images
Top, joint space in pixels
  Left
    JSA = 462
    min JSW = 6
  Right
    JSA = 154
    min JSW = 7
Bottom, angle in degrees
  FTA = 173.7
Test images show that Matlab program works on idealized images
Notes: koacad(FTA_test,5,1,1,800,5)

## Slide 11: Process: Boundaries
Vertical difference filter
  User control
  Threshold as percent of intensity
Upper: femoral condyle
Lower: tibial plateau
  Linear regression
Inner: intersection of regression line and tibia
Outer: lateral joint border
Notes: koacad(p_n6,12,1,1.05,800,3)

## Slide 12: Joint Space Characterization
Joint space width (JSW)
  Vertical distance in pixels
  Minimum JSW
    Left: mJSW = 7
    Right: mJSW = 7
Joint space area (JSA)
  Number of pixels
  Sum of all JSW
    Left: JSA = 682
    Right: JSA = 1076
Can normalize pixel values
Notes: koacad(p_n6,12,1,1.05,800,3)

## Slide 13: Joint Space Results
Successes
  Upper, lower, inner, and outer bounds identified
  More shading on lateral sides of joint
  Adjusting threshold for vertical neighbor difference
  Summing algorithm for Joint Space characterization
Difficulties
  Slanted alignment of images
  Background noise unfiltered
  Dimensions vary
  Manual zooming-in is labor intensive

## Slide 14: Joint Space Results
Left
JSA = 240
mJSW = 11
Right
JSA = 1377
mJSW = 11
Left
JSA = 371
mJSW = 5
Right
JSA = 808
mJSW = 5
Left
JSA = 23041
mJSW = 62
Right
JSA = 4869
mJSW = 60
Left
JSA = 10749
mJSW = 13
Right
JSA = 6746
mJSW = 26
Notes: koacad(n1,24,1,1.22,800,20)
koacad(n5,5,1.07,1.2,800,8)
koacad(ser5,5,1.02,1,800,5)
koacad(ser8,5,1,1,800,3) (takes a while)

## Slide 15: Test image: FTA
Top, results in pixels
  Left
    JSA = 462
    min JSW = 6
  Right
    JSA = 154
    min JSW = 7
Bottom, result in degrees
  FTA (femorotibial angle)
  = 173.7
Notes: koacad(FTA_test,5,1,1,800,5)

## Slide 16: Process: Midline Regression
Horizontal difference filter
  User control
  Intensity threshold
Medial regression lines
  Femur – blue
  Tibia – green
Notes: koacad(oa7,8,0.975,1,800,10)
koacad(oa7,8,0.975,1,800,5)

## Slide 17: Femorotibial Angle
Regression lines
  Slope m
    m1 – Femur , blue
    m2 – Tibia, green
  tan(FTA) = (m1 – m2)
  (1 + m1*m2)
  FTA = 169.4 degrees
Same limitations as JSA
  Intensity distribution
  Highly variable
Notes: koacad(oa7,8,0.975,1,800,5)

## Slide 18: Femorotibial Angle Results
FTA
= 172.8
FTA
= 176.4
Notes: koacad(oa5,6,0.88,1,800,5)
koacad(ser2,3,0.94,0.9,800,3) (takes a long time)

## Slide 19: Femorotibial Angle Results
FTA
= 169.6
FTA
= 155.8
Notes: koacad(ser7,5,1,1.1,800,3) (takes a long time)
koacad(n4,20,1,1.1,800,8)

## Slide 20: Combining analyses
Example of normal knee
Joint space evaluation
  Left
    JSA (joint space area) = 371
    min JSW (joint space width) = 5
  Right
    JSA = 808
    min JSW = 5
Femorotibial angle
  FTA = 171.2 degrees
Notes: koacad(n5,5,1.07,1.2,800,8)

## Slide 21: Combining analyses
Osteoarthritic knee
  Right joint space undetectable
Joint space evaluation
  Left
    JSA (joint space area) = 884
    min JSW (joint space width) = 7
  Right
    JSA = 19
    min JSW = 7
Femorotibial angle
  FTA = 169.4 degrees
Notes: koacad(oa7,8,0.975,1,800,10)
koacad(oa7,8,0.975,1,800,5)

## Slide 22: Conclusion
Numerical comparison of 2D x-rays
  Osteoarthritic mJSW and JSA pixel values
  FTA – angle of joint bones possible sign of osteoarthritis
Future improvements
  Osteophyte area, as done in KOACAD
  Image quality
    Intensity distribution
    Background signals
  Automation
    Filtering
    Threshold detection
    Atlas mapping
  Compare with 3D imaging

## Slide 23: References
Primary source:
Oka H, Muraki S, Akune T, Mabuchi A, Suzuki T, Yoshida H, Yamamoto S, Nakamura K, Yoshimura N, Kawaguchi H. Fully automatic quantification of knee osteoarthritis severity on plain radiographs. Osteoarthritis Cartilage. 2008 Nov;16(11):1300-6. Epub 2008 Apr 18.
Additional sources:
Oka H, Muraki S, Akune T, Nakamura K, Kawaguchi H, Yoshimura N. Normal and threshold values of radiographic parameters for knee osteoarthritis using a computer-assisted measuring system (KOACAD): the ROAD study. J Orthop Sci. 2010 Nov;15(6):781-9. Epub 2010 Nov 30.
Cooke TD. Re: "Fully automatic quantification of knee osteoarthritis severity on plain radiographs". Authors: H. OKA et al. Osteoarthritis and Cartilage (2008) 16, 1300-1306. Osteoarthritis Cartilage. 2009 Sep;17(9):1252-3; author reply 1254. Epub 2009 Mar 28.
Johansson A, Sundqvist T, Kuiper JH, Öberg PÅ. A spectroscopic approach to imaging and quantification of cartilage lesions in human knee joints. Phys Med Biol. 2011 Mar 21;56(6):1865-78. Epub 2011 Mar 1.
Dodin P, Pelletier JP, Martel-Pelletier J, Abram F. Automatic Human Knee Cartilage Segmentation from 3D Magnetic Resonance Images. IEEE Trans Biomed Eng. 2010 Jul 15. [Epub ahead of print]
Bowers ME, Trinh N, Tung GA, Crisco JJ, Kimia BB, Fleming BC. Quantitative MR imaging using "LiveWire" to measure tibiofemoral articular cartilage thickness. Osteoarthritis Cartilage. 2008 Oct;16(10):1167-73. Epub 2008 Apr 14.

## Slide 24: Knee X-ray Sources
Primary image source:
Dr. Braden Fleming, Coro Research Center
Additional osteoarthritic knee x-rays:
http://www.mayoclinic.com/images/image_popup/mcdc7_kneearthritis.jpg
http://4.bp.blogspot.com/_uC-1Is5ZK44/S-wAlZJ0X9I/AAAAAAAAAQY/w7KHexuDZqA/s1600/Knee%2520X-Ray.jpg
http://3.bp.blogspot.com/_vT13IccOEqM/TL87gkX7JGI/AAAAAAAAASo/8HLvpat1nvo/s1600/89.jpg
http://www.ispub.com/ispub/ijos/volume_5_number_1_27/patella_refashioning_during_tkr_in_patient_with_previous_bilateral_patellectomy_using_bone_cuts/tkr-fig1.jpg
http://www.ispub.com/ispub/ijos/volume_5_number_1_27/patella_refashioning_during_tkr_in_patient_with_previous_bilateral_patellectomy_using_bone_cuts/tkr-fig1.jpg
http://www.hipandkneespecialist.com/knee_arth1B%20Nourbash.gif
http://www.sciencephoto.com/images/showFullWatermarked.html/C0075866-X-Rays_of_Normal_and_Degenerative_Knees-SPL.jpg?id=670075866
http://www.hwbf.org/hwb/conf/mill1/981030.jpg
Additional normal knee x-rays:
http://img.photobucket.com/albums/v110/shanbhag/AchesandJoints/ANJ3-KneeXray-s.jpg
http://fiftyone43four.files.wordpress.com/2010/06/knee_xray_normal.jpg
http://imagecache6.allposters.com/LRG/30/3041/GZPBF00Z.jpg
http://www.sciencephoto.com/images/showFullWatermarked.html/C0075866-X-Rays_of_Normal_and_Degenerative_Knees-SPL.jpg?id=670075866
http://www.health.com/health/static/hw/media/medical/hw/h9991217.jpg
http://4.bp.blogspot.com/_aG90Nx5mMjw/TSI5OmNwlVI/AAAAAAAAB6s/ZHfANxI-m9A/s640/normal-knee-xray.jpg
http://www.hwbf.org/hwb/conf/mill1/981030.jpg
http://www.stryker.mudbugmedia.com/images/library/stryker_xrays/normal_knee_xray.jpg